## Slide 1
Fast 4x4 Matrix Accelerator
Integrated on a RISC-V SoC
By Sampath (USN: NNM23EC153)

## Slide 2
Standard CPUs struggle with heavy math like matrix multiplication, which is essential for AI and graphics.
A normal CPU executes instructions one by one sequentially.
To multiply a 4x4 matrix, the CPU must run a triple nested loop.
That requires 64 separate math operations.
Fetching and decoding these instructions wastes over 100+ clock cycles.
The Problem: Software is Slow

## Slide 3
Instead of forcing the CPU to do the math step-by-step, we built a custom "math engine" directly onto the chip.
100+
Cycles (Software Method)
Like 1 worker carrying 1 brick at a time.
1
Cycle (Hardware Method)
Like 16 workers carrying everything instantly.
Our Solution: Hardware Acceleration

## Slide 4
We didn't invent a new computer. We upgraded an existing RISC-V system cleanly.
The Brain: The RISC-V CPU still runs the main C program.
The Highway: We used the standard AXI4-Lite bus to connect our module.
The Swap: We replaced an unused "counter" peripheral with our Matrix Accelerator.
The Benefit: We didn't have to change any core CPU wiring or invent custom assembly instructions.
How It Fits Together (The SoC)

## Slide 5
No Math Clocks
We don't use a clock to step through calculations. We use raw wires and direct logic gates.
Like Water in a Pipe
As soon as the matrices enter the inputs, electricity flows through 16 parallel multiply-add trees instantly.
1 Clock to Save
The only time we use a clock is when we hit the "START" button to save the final answer into a register.
How the Math Actually Works
The secret to doing this in 1 cycle is Combinatorial Logic.

## Slide 6
Writing the C code to control this is a simple 5-step process:
1. Pack: Squash four 8-bit numbers into one 32-bit row.
2. Load: Send Matrix A and Matrix B to the hardware's memory addresses.
3. Trigger: Send a `1` to the START register.
4. Wait: Poll the DONE register (it finishes instantly).
5. Read: Pull the finished 16-bit answers back into the CPU.
How Software Talks to Hardware

## Slide 7
Status: All 7 tests passed on hardware.
Identity & Zero
Proved basic math rules work correctly in hardware (e.g., A * I = A).
Software Compare
Hardware answers perfectly matched the CPU's slow software answers.
Stress Test
Fired the computation 10 times rapidly in a loop; hardware never glitched.
Proof it Works (Verification)
We ran 7 strict tests on the real FPGA (Boolean Board) to ensure 100% accuracy.

## Slide 11
OUTPUT

## Slide 12
OUTPUT

## Slide 13
OUTPUT

## Slide 14
Conclusion
This project proves that offloading specific tasks to hardware achieves a massive 64x speedup, showing how custom logic can seamlessly integrate into Open-Source RISC-V systems.
Thank You!